## Slide 1: Fundamental Performance Limits in Image Registration By Dirk Robinson and Peyman Milanfar IEEE Transactions on Image Processing Vol. 13, No. 9, 9/2004
CS679: Pattern Recognition
Josh Gleason and Rod Pickens

## Slide 2: Topics
Example Application of Performance Limits
Image registration and errors
Parameter estimation and errors
Performance limits (bounds) of estimators
Cramer-Rao lower bound

## Slide 3: Robotic Helicopter to Inspect Fukushima Reactors
Purpose
  Fly through damaged buildings
Navigation Approach: SLAM
  Install stereo sensors on craft
  Stereo vision  3D model
  Fly through 3D model
Critical Algorithm
  Image registration
Issue: Probability of collision
  How much bias in position?
  How much variance in position?
Analyze Accuracy of SLAM
  Errors in image registration
Decision: Will or will not helicopter
  successfully perform inspection?
Wiki Commons: Digital Globe
Fukushima Facility Building
Helicopter: http://flickrhivemind.net/Tags/apache,lego

## Slide 4: Registration Errors
Errors
  Assume only translational errors
    Δx and Δy
  Higher order errors
    Not modeled
Asymptotic performance
  Bias
    E(Δx) ≠ 0 and E(Δy) ≠ 0
  Variance
    σ2 = E{(Δx+Δy)2} – E(Δx)E(Δy) > 0
  Errors: Δx and Δy > 0
WikiCommons: Jazzjohn, 2012

## Slide 5: Estimation: Accuracy and Precision
PDF: WikiCommons: Pekaje
Targets: www.caroline.com/teacher-resources
Target Practice
1D Error Distribution
(Bias)
(Variance)

## Slide 6: Performance Limits
How accurate? Bias
  Error about true position
How precise? Variance
  Error about mean of estimator
What is best? Optimal
  What are performance limits?
Is this best performance?
Targets: www.caroline.com/teacher-resources

## Slide 7: Registration Errors Impact Navigation (Image registration errors cause 3D world model errors)
Small Bias, Small Variance
Large Bias, Small Variance
Small Bias, Large Variance
Large Bias, Large Variance
Room 2: Fukushima Reactor
Damaged Wall
Enters Room 2: 3D mapping algorithm is a
minimum variance, unbiased estimator (MVUE).
Room 1: Fukushima Reactor
Damaged Wall
Collides with Wall: not MVUE algo
Enters Room 2: MVUE algo

## Slide 8: Minimum Variance, Unbiased Estimator: Cramer-Rao Lower Bound (CRLB)
Var(θ)
CRLB is a minimum
variance unbiased estimator
Best
CRLB is Best MVUE

## Slide 9: Modeling Registration Errors and CRLB
J=Fisher Information Matrix (FIM)
Log likelihood function as in Maximum Likelihood (ML) Estimation
)
Bias
Variance
MSE = Mean Square Error used as measure of registration error

## Slide 10: Registration, ML Estimation, and Objective Function
Log-likelihood function
f(m,n) = truth
v(m,n) = shift
ε(m,n) = Gaussian noise
Image courtesy Matlab
Imagery
Objective Function
Notes: Because only the second term contains unknown parameters v1 and v2, the problem of maximum likelihood is really a minimization of this term. The normalization by f^2 is normalizing by the energy of the cost.

## Slide 11: Deriving J(Φ) = FIM (Fisher Information)
Second partials of log likelihood
Expected value of second partials
=
=
Equating to x and to y

## Slide 12: The Fisher Information Matrix (FIM)
=
=
Given
The FIM is
Where
Notes: Notice the FIM is dependent on the structure of the image. This makes sense because variance on an image which is a smooth gradient will be very large while variance on a corner will be smaller. For those who have taking computer vision, this matrix is very similar to the harris corner detor’s structure tensor (second moment matrix) without the windowing.

## Slide 13: Results: Variance and Bias Errors
CRLB: MSE)
ASD: average square distance
DC: maximum direct correlator
Pyr: multiscale gradient-based
GB: gradient-based method
Proj-GB: project GB
Pyr-Proj: Project Pyr
Phase: relative phase
Flat: Estimator bias
Sloping: Estimator variance

## Slide 14: Conclusion
Variance of an estimator
Fisher Information
Cramer-Rao lower bound (CRLB)
  Quantitative measure of estimator performance
Application of CRLB to image registration
Notes: In this slide I will just reiterate what we have learned and what is important to take away from this presentation.